## Slide 1: Bonitron, Inc.
Dedicated to engineering quality industrial electronics since 1962!
20130806

## Slide 2: Introduction
Est. 1962
Drive enhancements compatible
with all major drive manufacturers
Maximize process uptime
Designed and manufactured
in the U.S.A.

## Slide 3: Introduction
Line Regeneration, Braking Transistors & Resistors, Single & 3 Phase DC power Supplies, Sag & Full Outage Backup for VFDs
Bonitron designs and manufactures industrial power electronic modules. We specialize in power electronic assemblies for manufacturers of Variable Frequency Drives and system integrators that support critical applications within many industries worldwide. Bonitron Variable Frequency Drive (VFD) Option Modules include Line Regeneration Modules, Dynamic Braking Transistors and Resistors, Power Loss Ride Thru Modules. These products allow variable frequency drive systems to operate effectively and avert faults and production system shut downs that are due to poor power quality or system dynamics. Bonitron equipment is sold and supported by the distribution and integration channels of major drives manufacturers.
Diode Modules, Capacitor Maintenance Products

## Slide 4: Why Use Bonitron
Bonitron compliments ANY drive line
Fill in accessory gaps for missing VFD options
Improved lead times
Simple DC bus connection
Manage VFD DC Bus Over Voltage & Under Voltage
Quality & Reliability
Strong reputation in multiple industries utilizing VFDs
Local design AND engineering support
Support

## Slide 5: Basic Drive Topology
3 Phase AC from Distribution
DC from the Input Converter is used to develop DC bus with the DC bus capacitors for the transistor output inverter
3 Phase AC is converted to DC for the Drives DC bus
The output inverter uses DC to make a sine wave (AC) for the motor
IGBTs that fire in a sequence that feeds the motor
Notes: Bonitron products work with any drive brand with DC +/- connections.

## Slide 6: Drive DC Bus Management
Standard Product Power - 3 AC Line and 2 DC Bus Connections
Standard Unit Connectivity Make’s New Installations or Retrofits Easy and Non-Invasive to The Drive…
WE WON”T VOID A DRIVES WARRANTY!
Our Products Support all Line Voltages Worldwide
Enable Circuits, Ethernet Comms. or Control Power Options May Add a Few More Connections for Some Products
Notes: Bonitron products work with any drive brand with DC +/- connections.

## Slide 7: External Braking Transistors
M3452
Heavy Duty Braking Transistors
75 Amps – 1600 Amps Single Unit
Network Options
230-690VAC
M3575T
30 Amps – 600 Amps
10-20% Braking Duty
230-460VAC
M3675T
20% Braking Duty
Fractional-10 Hp
115-460VAC
“Choppers”
7
Drive DC Bus Connections
M3452
10-33% Braking Duty
Up to 43Hp
115-460VAC
Combination Brake Resistor & Transistor
Notes: Bonitron has 3 series of braking transistors. Act as switch that allows overvoltage to flow into resistor to prevent drive faults.
Example – AB drive OV fault 810VDC, Bonitron Transistor turns on at 750VDC

## Slide 8: Braking Resistors
8
Braking Resistors
Drive DC Bus Connections
M3775R
10, 20, 50 & 100% Duty
Fractional to 1000 Hp+
230-690VAC
NEMA 3R
Vertical Air Flow
Multiple Resistive Elements
Case Resistors
56W – 11K Watts
Convection or Fan Cooled
NEMA-3R
Stainless Steel – 366, 316
Various Build Options
Multiple Elements in One Enclosure for Multiple Braking Transistors
Custom 3 Phase Load Banks
100% Duty 100Hp+ Modular Braking Resistors
10-20%, 50% or 100% Braking Duty
Case Resistors
1Hp–20Hp
IP 66 Wash Down
M3575R
6-20% Duty
33 Hp Peak
230VAC – 460VAC
Internal IGBT
External Brake Transistor
Notes: There’s no need to go anywhere but Bonitron for your braking solutions. You can get your transistor AND resistor from us.

## Slide 9: Line Regeneration Modules
M3545 and M3645 Line Regens
Features
Regenerative Energy From DC Over Voltage is Rectified and Returned to the AC Line at 99% Efficiency
Digital HIM Display with Regenerative Energy Event Logging for Energy Savings
M3545 - 6A, 15A, 150% Peak Rated for 60 Seconds
150% Overload for 60 Seconds
208 - 600VAC Support
50/60Hz auto select
100A, Below M3645 and M3545 Units Below Have Internal Line Reactors and Transient Surge Suppression MOVs
M3645 - 30, 50, 100, 150A, 225A and 300A Amp units
Greater Than 100A Units Have
Notes: 9
The Bonitron Line Regen takes the place of a braking transistor and resistor. Instead of dumping excess energy into a resistor, the Bonitron Line Regen returns that energy back to the AC line. This reduces room cooling requirements and has a smaller footprint.

## Slide 10: Common Bus Power Supplies
M3713SC & M3713DM Versions
Drives Powered Via DC +/-
Drives Share Power
Single Or 3-phase AC Input
Regenerative Energy Solution Can Be Sized To Cover Multiple Inverters
Can Be Configured For 12 And 18 Pulse Solution With Drive Converter
With And Without Drive Pre-charge. SC With, DM Without
AC In. DC Out
M3713 Common Bus Power Supply
Notes: Common Bus Power Supply
Using a common bus power supply reduces the amount of wiring and components in a system, resulting in a reduction of maintenance and footprint of the system. In a system with multiple motors, some motors may be regenerating while others are motoring. The common bus allows the regenerating drives to share power with the motoring drives, thus reducing the amount of power needed from the grid. If the drives are creating a net surplus of energy, a single line regen or braking unit can be installed to dissipate the excess energy.

## Slide 11: Common Bus Power Supplies & Regen
Common Bus PS Features
DC Bus Can Share Circulating Energy
Only VFD DC Fed Inverters Required
M3713SC Or M3713DM With M3645 Line Regen
Sized to Total regen Current On DC Bus With Multiple Drive Common Bus
SC Version - Single Pre-charge for Multiple Drives
Regenerative Energy is returned to The Line at 99% Efficiency from Entire Common Bus
M3713SC & Line Regen
3 Phase AC Drive Input
Multiple Drive DC Bus

## Slide 12: Regenerative Power Supply
M3545P & M3645P Line Regen
M3645P – 30A, 50A, 100A, 300A
Only Drives Inverter Section is Required
Separate Pre-charge Module Option
No Diode Sharing is Required
Internal Line Reactor 5% 30 to 100A Units
300A Separate Line Reactor, Choke
AC & DC Fusing Kits (less $$)
M3545P – 15A 100%
150% 60 Seconds
22A Peak for 60 Seconds
MOV Module
Turns Standard Drive Regenerative
M3545P & M3645P Regen Power Supply
Power Supply + Line Regen in A Single Unit
3 Phase AC Drive Input
Multiple Drive DC Bus

## Slide 13: M3712 Single Phase Power Supply
M3712 Single Phase Power Supply
3-phase Drives/Motors Must Be De-rated 50-70% for Use With Single Phase Power
Output Drive DC Bus Power
Can Parallel
Input 230VAC and 460VAC
Multiple DC Bus Connected Drive One M3712
With the M3712 Single Phase Power Supply, NO Drive or Motor De-rate Needed
30, 50, 75, 125Hp
Drive De-rating NOT Required
Notes: Technically, Bonitron offers another Common Bus Power Supply, however this 3712 Series is specifically for those with only single phase AC power.
The M3712 Single Phase Power Supply takes a single phase AC input and outputs DC voltage that will power the DC +/- terminals of an AC drive.
Normally, users must buy a 3-phase drive 2-3 times larger than necessary if they are going to power it with only single phase power. Many drive manufacturers do not recommend this as it can decrease the drive’s life and jeopardize UL status.
For example:
A 50HP application would require a much more expensive 100-150HP 3-phase drive.
But with Bonitron a 50HP applicaton would require a line reactor, 50HP M3712 unit, 50HP drive.

## Slide 14: Common Bus Diode Sharing
Sharing Diodes
Common Drive DC Bus
M3345CBM
Separate AC Feeds For Each Drive Rectifier
Diode Drops on DC+ and DC
Diodes Help Control Circulating Currents From Larger Drives For Protecting Smaller Drives on DC Bus During Pre-charge
Single Over Voltage or Under Voltage Solution Can Cover Total Of Drives On The Common Bus
3 Phase AC Line Separate Drive Feeds
Multiple Drives Individual AC Feeds
Line Regen Unit,
Brake Transistor &
Resistor or UPD
M3345CBM Bi-Directional Diode Modules
Notes: Common Bus Sharing Diodes M3345CBM
If drives on the AC line are connected by a DC bus, circulating currents can be created that might cause drive faults. The sharing diodes allow a two way flow of power to and from drives enabling them to share power between their DC busses while preventing circulating currents. The two-way flow allows the drives to share power with each other and use a common braking, regen, or UPD.
Common Bus Isolation Diodes M3345D, M3460D
Unlike the sharing diodes, the isolation diodes allow only a one-way flow of power and do not allow drives to share power with each other, completely isolating the drives and preventing circulating currents. The isolation diodes allow multiple drives to be connected on the DC bus so that they can share one braking unit, regen, or UPD. The M3345D allows an outward flow of power from the connected drives to be dissipated by a braking or regen unit. The M3460D allows inward flow of power so that one UPD can power all of the drives connected to the DC bus.

## Slide 15: Determining Your Solution
Questions for Customers
What Bonitron Needs To Know for a DC Bus Over Voltage Management Solution
AC Line Voltage
Drive Hp or Hps or kW
Braking Duty Cycle or Overhauling Period Time In Relation to One Process Cycle in Percentage?
Common Bus Drives or Stand Alone?
Peak Braking Power (Braking Torque)?
Internal Braking Transistors Minimum Ohm Value?
Common Bus Drives All Fed AC Separately?
Deceleration
Overhauling
Combination

## Slide 16
16
Critical Process Drives Under Voltage Protection
Utility Power Can Be Lost In An Instant…
Fallen Trees
Flooding
Lightning Strikes
Mother Nature
Human Nature
Slide
34
AC Line Loss (Utility Power)
Brown Out

## Slide 17: Critical Process Protection
Plant Backup Systems & Redundancy
Solution selection is usually dependent on the critical nature of an application. In critical applications, several levels of plant process and drive/motor protection are required. “Redundancy Levels”.
This is common in applications such as Semiconductor and Data Center HVAC VFD Systems where no change in speed or torque of the associated motor can occur.
Power Distribution UPS
Plant Gen Set
Process Level VFD Backup
Plant Redundancy

## Slide 18
Critical Process Backup Reasons
Personnel Safety Can Be Compromised if the Associated Process Motor Losses Power and Becomes Erratic
Data Centers – Environmental Systems Backup
Critical Process Examples
Semiconductor – Cleanroom Air Handlers & Machine Tool Chill Water
Lubrication Systems
Safety Systems
Security Gates
Loss of Security System Power Can Allow Intrusion Into High Security Areas
Loss of Power to Equipment’s Personnel Safety Features Can Create Hazzard to Workers
Hoists & Cranes Can Drop Load
Power to Security Access Areas is Cut During Breach Attempts
Robotics Multi Axis Systems Lose Reference Causing Damage to Mechanical Components or Surrounding Equipment
High Speed Turbines Can Burn up Without Constant Lubrication
Cleans Rooms Must Remain Free of Environmental Particulates or Expensive Semiconductor Wafers are Discarded
Machine Tools for Wafer Etching Must maintain Constant Chill Water Cooling Due to High Speed Operation
Any Slight Deviation in Motor Speed or Torque Can Create Scrap Product and Expensive Production Loses or Cleanup
Critical Data Can Be Lost if Environmental Systems Are Lost and Data Servers Overheat
Chemical and Toxic Exhaust Ventilation
Loss of Ventilation and Exhaust Fans can Create Personnel Hazzard from Toxic Gases
Perishable Products can Be Lost During AC Line Loss that Can Trip Refrigeration Compressor VFDs/Motors
What is a Critical Process?
Critical Process Protection

## Slide 19: UPD Enclosures & Configurations
19
M3534R + Ucaps – 0.5-3 Seconds AC Line Loss
M3460R + Ucaps – 0.5-3 Seconds AC Line Loss
M3800 Regen Bidirectional Capacitor Controller
24VDC, 120VAC Control Power Ride Thru
S3534SR – 2-3 Second 60% Sags – 10-50kW
S3460SR – 2-3 Second 60% Sags – 50-250kW+
S3534UR, S3460UR – 3-15 Seconds – 10-250kW
S3534BR, S3460BR –15 Seconds to 60+ Minutes – 10-250kW+
UPD – Uninterruptable Power For Drives
M3534B/M3460B (HD Booster) Ultracapacitor 3-15 Seconds
M3534B/M3460B + Batteries 15 Seconds to 60 Minutes +
15 Seconds to 60 Minutes
0.5 to 15 Seconds
M3460D UPD RT Common Bus Diodes
UPD Sag Cabinet Systems
UPD Integratable Sag Modules
UPD Multiple Drive Solution
M3534R 2-3 Seconds 60% Sags
M3460R 2-3 Seconds 60% Sags
UPD 100% AC Line Loss Integratable Modules
0.5-3 Second 100% AC Line Loss Modules
UPD 100% AC Line Loss Cabinet Systems
Control Power Backup
Sags & Outages
Notes: Bonitron has 3 series of braking transistors. Act as switch that allows overvoltage to flow into resistor to prevent drive faults.
Example – AB drive OV fault 810VDC, Bonitron Transistor turns on at 750VDC

## Slide 20: UPD – Uninterruptable Power For Drives
20
Sag Protection
AC Line Outage Protection
Up to 250kW Single Unit.
3 Phase 3 Second Sags
40% AC Line Remaining
Up to 250kW Single Unit
0.5 Seconds to Minutes 100% AC Line Loss
Model Number Designators
M = Module
S = System
BR = Batteries
SR = Sag RT
UR = Ultracapacitor
CR = Low Hp Electrolytic Caps
EC = Low Hp Electrolytic Caps
UPD Product Number Selection
Full Cabinet Systems Are Designated With An “S”
Integratable Modules Are Designated With
An “M”
Part Number Breakdown
M3460R-H100-R9-F
V/R Booster Type
AC Line
H-480VAC
E-380-415VAC
C-600VAC
Max
kW
Open Chassis
Type
Fusing
Integratable Modules

## Slide 21: UPD – Uninterruptable Power For Drives
AC Input To VFD During Sag
Sags Are a Partial AC Line Loss
VFD DC Bus With Ride Thru
No Affect Seen By Process Flow Meters Or Sensors
VFD Does Not See Change In Motor Speed or Torque
A Single Voltage Regulator Booster Can Cover 60% Sags/40% Remaining 3 Phase AC Line for 2-3 Seconds
100% Single Phase AC Line Loss with 40% Total AC Line Remaining 2 Phases
100% 3 Phase AC Line Loss Requires Additional Energy Storage
Sags Are Not The Whole Problem. Returning AC Can Create Surges.
AC Line Sag with DC Bus Ride Thru
M3460R 50kW-250kW
M3534R 10kW-50kW
Notes: 21

## Slide 22: UPD – Uninterruptable Power For Drives
Power Connections AC and DC
D5 Power Supply PCB
M6 Interface PCB
C1 Control PCB
Ride Thru Bus Capacitors & IGBTs
Diode Isolation
Voltage Regulator Booster

## Slide 23: UPD Display Options
Records Menu
View Ride Thru Event Statistics Or Individual Event Records
Actions Menu
Threshold Check
DC Bus Voltage Fault Logic
TEST Initiate
The System Ships With Records Of A Single Event Initiated During Checkout
RT Event Parameters
100 Most Recent Fault States
Configurations Menu
Set Time
Set Status Timer
  Green – Power
  Amber – Ride Thru / Charger Active
  Red – Fault

## Slide 24
Short Term Energy Storage
Ultracapacitor Energy Storage
Electrolytic Capacitor Energy Storage
0.5 – 15 Seconds 100% 3-phase outages,
Less Than 15kW
Greater Than 15kW
Less Than 0.5 Sec
VR - Voltage Regulator
CH - Charger
CAP - Capacitors
DCH - Discharger
60Hp 1 Second Full AC Line Loss Ultracapacitor Energy Storage Included
150kW 1 Second Full AC Line Loss Ucap Energy Storage Included in Adjoining Bay
AC Line Short Term Outage
UPD – Uninterruptable Power For Drives

## Slide 25: UPD – Uninterruptable Power For Drives
Long Term Energy Storage
15 Seconds - Minutes 100% 3-Phase Outages
Battery Energy Storage
VRLA Standard, Other Battery Types Available
Does Not Require Discharger
VR - Voltage Regulator Booster
CH - Charger
B - Battery Energy Storage
230VAC, 50kW
30 Seconds Battery Energy Storage Included
460VAC, 250kW
15 Minutes
Battery Energy Storage
AC Line Long Term Outage

## Slide 26: Determining Your Solution
Questions for Customers
What Bonitron Needs To Know for a Drive Under Voltage Solution
AC Line Voltage
Drive Hp or Multiple Drive Total Hps or kW
Sag or 100% AC Line Loss
Common Bus Drives or Stand Alone
Sag – Percent & Time AC Line Lost
Internal Braking Transistors Minimum Ohm Value
100% 3 Phase Outage Time – Greater Than 50%, Energy Storage
50% Sag, 50% Remaining - Single Voltage Regulator Booster
Sag – 50% AC Line
2s or Less
Outage – 100% AC Line
10s or Less (kW Dependent)
Outage – 100% AC Line
10s or Greater (kW Dependent)

## Slide 27: Bonitron Maintenance Advantage
Bonitron Equipment Requires Very Minimal Maintenance.
Maintenance Includes A Short Test And Monitoring LEDs And The DD5 Display When Required.
Bonitron Equipment Is A Parallel Solution.
Bonitron UPD Equipment Does Not Pass All The AC To The VFD As Does A Series Solution Tied To The Input Of The VFD, This Greatly Extends Product Life, Reduces Energy Losses and Improves Efficiency.
It Is Activated For A Few Minutes And Remains In A Static State Waiting For The Next RT Event Using Much Less Energy Than A Series AC Input Solution.

## Slide 28: Maintenance Solutions
Battery Testers
Rapidly tests M3528B Battery Modules
Capacitor Dischargers
Depletes energy stored in ultracapacitors
Capacitor Formers
Form capacitors
Benchtop power supply
Capacitor Testers
Measure capacitance and ESR to determine when
end of life is reached
https://www.youtube.com/watch?v=lzH7dbczeZ4&t=5s
https://www.youtube.com/watch?v=543rPcwyqis&t=11s
PCF Operation Video
ACF Operation Video

## Slide 29: Who Uses Bonitron
Drives
Motion
Control
Servo Drives
Inverters
Converters
Braking
Transistors
Isolation
Transformers
Seek customers that use or integrate drive components

## Slide 30
Major Applications History

## Slide 31: For More Information…
615-244-2825
Visit The Web site www.Bonitron.com
info@bonitron.com
Questions?
Training Videos
Manuals
Brochures
Unit Specifications
Contact Info
https://bonitron.com/PDFs/Manuals/Product_Overview_update_web_05_07_2024_new1.pdf
Complete Product Overview

## Slide 32
Dedicated to Designing and Manufacturing
Quality Industrial Electronics
BONITRON
WWW.BONITRON.COM
-
615-244-2825